## Slide 1: Fresno Council of Governments Measure C Steering Committee
Impacts of Measure C Renewal
July 10, 2025
Notes: Paul or Robert – please edit as needed

## Slide 2: Questions We Are Answering Today
  How many miles of streets are in Fresno County?
  What condition are they in?
  What repairs are needed in the next 25 years?
  How much funding is needed?
  How does Measure C help?

## Slide 3: Local Street Network in Fresno County
Total Value = $6.0 Billion

## Slide 4
How is Pavement Condition Measured?
0
100
70
50
25
Very Poor/Failed
Poor
Good/Very Good
Fair
Condition Category
Pavement Condition Index (PCI)
Notes: We will delete this slide if we cannot get graphic of the left

## Slide 5
How is Pavement Condition Measured?
0
100
70
50
25
Very Poor/Failed
Poor
Good/Very Good
Fair
Condition Category
Pavement Condition Index (PCI)

## Slide 6: What Condition Are Streets In?
Chart: PCI
| Clovis | Parlier | Kerman | Sanger | Fresno County | Kingsburg | Fowler | Selma | Coalinga | Fresno | Firebaugh | Reedley | Huron | Mendota | Orange Cove | San Joaquin
2025 PCI | 71 | 69 | 66 | 66 | 66 | 65 | 63 | 59 | 58 | 55 | 54 | 51 | 42 | 39 | 33 | 31
2022 Statewide & 2026 Countywide average

## Slide 7: PCIs of Other Cities & Counties
2022 Statewide & Countywide: 65
Chart: PCI
| Los Angeles | San Joaquin County | Fresno County | Bakersfield | Stanislaus County | Kern County | Kings County | Sacramento | Tulare County | Sacramento County | Merced County | Mariposa County | Madera County | San Benito County
PCI | 69 | 68 | 65 | 64 | 64 | 63 | 61 | 59 | 59 | 58 | 57 | 51 | 40 | 38
Counties include cities

## Slide 8: Typical Construction Costs
0
10
20
30
40
50
60
70
80
90
100
Pavement Condition Index
Percent of Pavement Service Life
No Repairs Needed
Minor Resurfacing
Major Resurfacing
Reconstruction
Thin Overlays
$28-$61/SY
Thick Overlays
$57-$90/SY
Reconstruction
$90-$133/SY
Good 70-100
Fair 50-69
Poor 25-49
Very Poor 0-24
90%
75%
35%
Preventive Maintenance
Seals
$10-$17/SY

## Slide 9
Overlays
Increased 47% - 58% from 2022
Trends in Construction Costs

## Slide 10: Significant Changes since 2021
Countywide PCI has increased to 65 since 2021
  2021 – Fresno & County not surveyed by NCE at the time
  County’s PCI 6 points higher in 2025
Unit costs have increased significantly since 2021/22
  Seals – 47%
  Overlays – 47% to 58%
  Reconstruction – 25%

## Slide 11: Future Funding Assumptions
Road Maintenance and Rehabilitation Act (RMRA) aka SB1
  Reduction of 6% annually until 2035, then flat thereafter
Surface Transportation Block Grant (STBG)
  Federal funding to grow 3% annually
Measure C
  Estimate (2027/28) approx. $126.3 Million/year
  Grows by 3% annually
  30%, 40%, 50% and 60% allocated to local roads
2025 Est. Funding = $162 M/year
Chart: 
| STBG | HUTA and RMRA (SB1) | Measure C
 | 23062565.8 | 104867507.99 | 34134181.78
Notes: Update pie chart and 2025 existing funding
Thanks for providing the Measure C base estimate. I did some simple calculations, and the cumulative Measure C with 3% inflation will be $3,394,571,463 (SC1) and $6,010,267,873 (SC2) for 20 years and 30 years, respectively. I am going to run four scenarios for each, considering that 30%, 40%, 50%, and 60% of Measure C will go towards road maintenance. Am I heading in the right direction?
I talked with our Finance Director this morning and for our base year Measure C estimate (2027-28) we are looking at $126,331,379. This would be the base number to use for the 3% annual inflation rate.

## Slide 12: Estimated Funding (20-Year)
Chart: Year
| FY25-26 | FY26-27 | FY27-28 | FY28-29 | FY29-30 | FY30-31 | FY31-32 | FY32-33 | FY33-34 | FY34-35 | FY35-36 | FY36-37 | FY37-38 | FY38-39 | FY39-40 | FY40-41 | FY41-42 | FY42-43 | FY43-44 | FY44-45 | FY45-46 | FY46-47 | FY47-48 | FY48-49 | FY49-50
STBG | 23.1 | 23.8 | 24.5 | 25.2 | 26 | 26.7 | 27.5 | 28.4 | 29.2 | 30.1 | 31 | 31.9 | 32.9 | 33.9 | 34.9 | 35.9 | 37 | 38.1 | 39.3 | 40.4 | 41.7 | 42.9 | 44.2 | 45.5 | 46.9
SB1 | 104.9 | 98.6 | 92.7 | 87.1 | 81.9 | 77 | 72.3 | 68 | 63.9 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1
Current Measure C | 34.1 | 34.1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
30% Over 20 Years | 0 | 0 | 37.9 | 39 | 40.2 | 41.4 | 42.7 | 43.9 | 45.3 | 46.6 | 48 | 49.5 | 50.9 | 52.5 | 54 | 55.7 | 57.3 | 59 | 60.8 | 62.6 | 64.5 | 66.5 | 0 | 0 | 0
40% Over 20 Years | 0 | 0 | 12.6 | 13 | 13.4 | 13.8 | 14.2 | 14.6 | 15.1 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.6 | 19.1 | 19.7 | 20.3 | 20.9 | 21.5 | 22.2 | 0 | 0 | 0
50% Over 20 Years | 0 | 0 | 12.6 | 13 | 13.4 | 13.8 | 14.2 | 14.6 | 15.1 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.6 | 19.1 | 19.7 | 20.3 | 20.9 | 21.5 | 22.2 | 0 | 0 | 0
60% Over 20 Years | 0 | 0 | 12.6 | 13 | 13.4 | 13.8 | 14.2 | 14.6 | 15.1 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.6 | 19.1 | 19.7 | 20.3 | 20.9 | 21.5 | 22.2 | 0 | 0 | 0
Total Pavement Funding: $4.65B
(Measure C is $1-2 B)

## Slide 13: Estimated Funding (30-Year)
Chart: Year
| FY25-26 | FY26-27 | FY27-28 | FY28-29 | FY29-30 | FY30-31 | FY31-32 | FY32-33 | FY33-34 | FY34-35 | FY35-36 | FY36-37 | FY37-38 | FY38-39 | FY39-40 | FY40-41 | FY41-42 | FY42-43 | FY43-44 | FY44-45 | FY45-46 | FY46-47 | FY47-48 | FY48-49 | FY49-50 | FY50-51 | FY51-52 | FY52-53 | FY53-54 | FY54-55 | FY55-56 | FY56-57
STBG | 23.1 | 23.8 | 24.5 | 25.2 | 26 | 26.7 | 27.5 | 28.4 | 29.2 | 30.1 | 31 | 31.9 | 32.9 | 33.9 | 34.9 | 35.9 | 37 | 38.1 | 39.3 | 40.4 | 41.7 | 42.9 | 44.2 | 45.5 | 46.9 | 48.3 | 49.7 | 51.2 | 52.7 | 54.3 | 55.9 | 57.6
SB1 | 104.9 | 98.6 | 92.7 | 87.1 | 81.9 | 77 | 72.3 | 68 | 63.9 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1 | 60.1
Current Measure C | 34.1 | 34.1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
30% Over 30 Years | 0 | 0 | 37.9 | 39 | 40.2 | 41.4 | 42.7 | 43.9 | 45.3 | 46.6 | 48 | 49.5 | 50.9 | 52.5 | 54 | 55.7 | 57.3 | 59 | 60.8 | 62.6 | 64.5 | 66.5 | 68.5 | 70.5 | 72.6 | 74.8 | 77 | 79.4 | 81.7 | 84.2 | 86.7 | 89.3
40% Over 30 Years | 0 | 0 | 12.6 | 13 | 13.4 | 13.8 | 14.2 | 14.6 | 15.1 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.6 | 19.1 | 19.7 | 20.3 | 20.9 | 21.5 | 22.2 | 22.8 | 23.5 | 24.2 | 24.9 | 25.7 | 26.4 | 27.3 | 28 | 28.9 | 29.8
50% Over 30 Years | 0 | 0 | 12.6 | 13 | 13.4 | 13.8 | 14.2 | 14.6 | 15.1 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.6 | 19.1 | 19.7 | 20.3 | 20.9 | 21.5 | 22.2 | 22.8 | 23.5 | 24.2 | 25 | 25.7 | 26.5 | 27.2 | 28.1 | 28.9 | 29.8
60% Over 30 Years | 0 | 0 | 12.6 | 13 | 13.4 | 13.8 | 14.2 | 14.6 | 15.1 | 15.5 | 16 | 16.5 | 17 | 17.5 | 18 | 18.6 | 19.1 | 19.7 | 20.3 | 20.9 | 21.5 | 22.2 | 22.8 | 23.5 | 24.2 | 24.9 | 25.7 | 26.4 | 27.3 | 28.1 | 28.9 | 29.7
Total Pavement Funding: $5.08B
(Measure C is $1.8 - $3.6 B)

## Slide 14: Funding Scenarios
Scenario 1: Measure C sunsets in 2027
Scenario 2: Measure C renewed (30%)
Scenario 3: Measure C renewed 20 years
Scenario 4: Measure C renewed 30 years
What are impacts on road conditions?

## Slide 15: PCI Forecast
Chart: Year
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049
Scenario 1 | 65 | 64 | 63 | 62 | 60 | 60 | 59 | 58 | 57 | 56 | 56 | 55 | 54 | 54 | 53 | 53 | 52 | 52 | 51 | 50 | 50 | 49 | 48 | 48
Chart: 
| Good | Fair | Poor | Very Poor
 | 37.6 | 25.8 | 5.3 | 31.4
Chart: 
| Good | Fair | Poor | Very Poor
 | 44.2 | 25.5 | 22.8 | 7.5
Chart: 

## Slide 16: PCI Forecast
Chart: Year
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049
Scenario 1 | 65 | 64 | 63 | 62 | 60 | 60 | 59 | 58 | 57 | 56 | 56 | 55 | 54 | 54 | 53 | 53 | 52 | 52 | 51 | 50 | 50 | 49 | 48 | 48
Scenario 2 (20-Year) | 65 | 64 | 64 | 63 | 62 | 62 | 61 | 61 | 61 | 60 | 60 | 60 | 60 | 60 | 59 | 60 | 59 | 59 | 58 | 58 | 57 | 56 | 56 | 55
Scenario 2 (30-Year) | 65 | 64 | 64 | 63 | 62 | 62 | 61 | 61 | 61 | 60 | 60 | 60 | 60 | 60 | 59 | 60 | 59 | 59 | 58 | 58 | 57 | 57 | 56 | 56
Chart: 
| Good | Fair | Poor | Very Poor
 | 37.6 | 25.8 | 5.3 | 31.4
Chart: 
| Good | Fair | Poor | Very Poor
 | 51.1 | 22.6 | 3.5 | 22.7
Chart: 
| Good | Fair | Poor | Very Poor
 | 44.2 | 25.5 | 22.8 | 7.5
Chart: 

## Slide 17: PCI Forecast
Chart: 
| Good | Fair | Poor | Very Poor
 | 37.6 | 25.8 | 5.3 | 31.4
Chart: 
| Good | Fair | Poor | Very Poor
 | 51.1 | 22.6 | 3.5 | 22.7
Chart: 
| Good | Fair | Poor | Very Poor
 | 44.2 | 25.5 | 22.8 | 7.5
Chart: Year
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049
Scenario 1 | 65 | 64 | 63 | 62 | 60 | 60 | 59 | 58 | 57 | 56 | 56 | 55 | 54 | 54 | 53 | 53 | 52 | 52 | 51 | 50 | 50 | 49 | 48 | 48
Scenario 2 (20-Year) | 65 | 64 | 64 | 63 | 62 | 62 | 61 | 61 | 61 | 60 | 60 | 60 | 60 | 60 | 59 | 60 | 59 | 59 | 58 | 58 | 57 | 56 | 56 | 55
Scenario 2 (30-Year) | 65 | 64 | 64 | 63 | 62 | 62 | 61 | 61 | 61 | 60 | 60 | 60 | 60 | 60 | 59 | 60 | 59 | 59 | 58 | 58 | 57 | 57 | 56 | 56
Scenario 3 (50%) | 65 | 65 | 64 | 64 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 64 | 64 | 64 | 65 | 64 | 64 | 63 | 63 | 63 | 62 | 61 | 60
Scenario 4 (50%) | 65 | 65 | 64 | 64 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 64 | 64 | 64 | 65 | 64 | 64 | 63 | 63 | 63 | 62 | 62 | 62

## Slide 18: PCI Forecast
Chart: 
| Good | Fair | Poor | Very Poor
 | 37.6 | 25.8 | 5.3 | 31.4
Chart: 
| Good | Fair | Poor | Very Poor
 | 51.1 | 22.6 | 3.5 | 22.7
Chart: 
| Good | Fair | Poor | Very Poor
 | 44.2 | 25.5 | 22.8 | 7.5
Chart: 
| Good | Fair | Poor | Very Poor
 | 62.2 | 24.3 | 0.3 | 13.2
Chart: Year
| 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045 | 2046 | 2047 | 2048 | 2049
Scenario 1 | 65 | 64 | 63 | 62 | 60 | 60 | 59 | 58 | 57 | 56 | 56 | 55 | 54 | 54 | 53 | 53 | 52 | 52 | 51 | 50 | 50 | 49 | 48 | 48
Scenario 2 (20-Year) | 65 | 64 | 64 | 63 | 62 | 62 | 61 | 61 | 61 | 60 | 60 | 60 | 60 | 60 | 59 | 60 | 59 | 59 | 58 | 58 | 57 | 56 | 56 | 55
Scenario 2 (30-Year) | 65 | 64 | 64 | 63 | 62 | 62 | 61 | 61 | 61 | 60 | 60 | 60 | 60 | 60 | 59 | 60 | 59 | 59 | 58 | 58 | 57 | 57 | 56 | 56
Scenario 3 (50%) | 65 | 65 | 64 | 64 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 64 | 64 | 64 | 65 | 64 | 64 | 63 | 63 | 63 | 62 | 61 | 60
Scenario 4 (50%) | 65 | 65 | 64 | 64 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 64 | 64 | 64 | 65 | 64 | 64 | 63 | 63 | 63 | 62 | 62 | 62
Scenario 3 (60%) | 65 | 65 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 65 | 65 | 65 | 66 | 67 | 67 | 67 | 67 | 66 | 66 | 66 | 65 | 64 | 64 | 63
Scenario 4 (60%) | 65 | 65 | 64 | 64 | 64 | 64 | 64 | 64 | 64 | 65 | 65 | 65 | 66 | 67 | 67 | 67 | 67 | 66 | 66 | 66 | 65 | 65 | 65 | 65

## Slide 19: Unfunded Maintenance
Chart: Year
| 2025 | 2030 | 2035 | 2040 | 2045 | 2049
Scenario 1 | 1.6 | 2 | 2.4 | 2.8 | 4.1 | 5
Scenario 2 | 1.6 | 1.8 | 1.9 | 2 | 2.8 | 3.3
Scenario 3 | 1.6 | 1.7 | 1.5 | 1.1 | 1.7 | 2.4
Scenario 4 | 1.6 | 1.7 | 1.5 | 1.1 | 1.7 | 1.8
+ ($3.61 B)
+ ($2.04 B)

## Slide 20: Summary
Pavements represent a substantial investment ($6.0 Billion) in County
Pavement network is in Fair condition (PCI = 65 in 2026)
Scenario 1:
  If Measure C Sunsets in 2027, the countywide PCI will decrease to 48
Scenario 2:
  Measure C is renewed (30%) - PCI drops to 56
Scenario 3:
  Measure C is renewed for 20 years (50 & 60%) – PCI will be 60 and 63, respectively.
Scenario 4:
  Measure C is renewed for 30 years (50% & 60%) – PCI will be 62 and 65, respectively.
Improving PCI will require additional funding

## Slide 21
Margot Yapp, PE
MYapp@ncenet.com
Shahram Misaghi, PE
SMisaghi@ncenet.com